## Slide 1: Opti-Tool: Introduction
Overview of the planning and implementation options

## Slide 2: Presenter
  Khalid Alvi
  Environmental Engineer
  Tetra Tech, Incorporated
  Fairfax, Virginia
DISCLAIMER
The information presented in this webinar is intended solely to help parties understand the obligations and requirements imposed by MS4 permits. This webinar is not intended, and cannot be relied upon, to create any rights, substantive or procedural, enforceable by any party in litigation with the United States. EPA reserves the right to act at variance with the information presented in this webinar at any time without public notice.

## Slide 3: Project Background
Small MS4 General Permit for MA and NH
  Phosphorus reduction requirement to meet the Waste Load Allocations for the impaired watershed
Phosphorus Control Plan (PCP)
  To measure compliance with its phosphorus reduction requirement under the permit
  Opti-Tool
  A tool to facilitate storm water engineers to developing Nutrient Management Plans such as PCP

## Slide 4: Project Background – cont.
Proven benefits of optimization techniques in stormwater management
  Charles River watershed study
Practical needs by stormwater practitioners
  BMP simulation
  BMP optimization
  Independent of ArcGIS
  Simple to use

## Slide 5: Opti-Tool
A spreadsheet-based BMP optimization tool
  Planning Level Analysis (EPA Region 1 BMP Performance Curves)
  Implementation Level Analysis (EPA SUSTAIN BMP Simulation and Optimization Engine)
  Customized for EPA Region 1

## Slide 6: Opti-Tool: Planning and Implementation Options
Excel Inputs
Planning Level Input:
Target pollutant load reduction
Watershed land use area
BMP drainage area
Optimization method
Implementation Level Input:
Watershed, land use, pollutants
Potential BMPs representation
BMP treated area
Management objective
Output Postprocessor:
Cost-effectiveness solution
Optimal management options
BMP size and cost
Treated impervious area
Output Postprocessor:
Cost-effectiveness curve
Optimal management options
BMP type, size, and cost
Excel Outputs
Excel Solver
SUSTAIN Optimization Engine
Input
Text File
BMP Performance Curve

## Slide 7: Opti-Tool: Example Applications
Planning Level Analysis
  Maximum possible load reduction for all feasible BMP opportunities
    Watershed scale and/or site scale
    Aggregated BMP representation (grouping same BMP types as one unit)
    No BMP nesting (parallel BMPs)
  Cost-effective single solution meeting the numeric target
Implementation Level Analysis
  Optimal combination of different BMP types, sizes, and spatial locations
    Watershed scale and/or site scale
    Aggregated and/or distributed BMP representation
    simple to complex BMP routing network (BMPs in parallel and/or in series)
  Cost-effective solutions (CE-curve) for a range of load reduction targets

## Slide 8: Opti-Tool: Region Specific Data
Precipitation Representation
  Long-term hourly data at Logan airport (1992 – 2014)
Land Representation
  Stormwater monitoring data to calibrate the buildup & washoff processes on impervious cover
  Long-term landuse specific annual average load export rates
BMP Representation
  University of New Hampshire Stormwater Center (UNHSC) BMP monitoring data to calibrate flow and pollutant loss mechanism in BMPs
  Representative BMP cost information with scaling function

## Slide 9: Opti-Tool: Precipitation Analysis
Data Used
  12 weather stations from major urban areas
    Represents climate regions in New England states
  NCDC hourly weather records
Summary Results
  Average annual precipitation varies from 34 in. to 46 in. with average value of 42.3 in.
  Similar precipitation frequency distribution
    48 percent of the events are < 0.1 inch
    45 percent of the events are 0.1 to 1.0 inch
    7 percent are > 1.0 inch
  Boston Logan Airport station is representative

## Slide 10: Opti-Tool: Buildup & Washoff Calibration
Data Used
  National Stormwater Quality Database (NSQD)
  Massachusetts and New Hampshire sites
  100% impervious drainage areas
  Storm events smaller or equal than 1 inch
  Pollutants (TP and TN)
Buildup & Washoff Parameterization
  Developed computer codes using GA algorithms to identify the parameter pattern that best fit the observed data
  Calibrated 21 sets of parameters representing different initial conditions
  Performed sensitivity analysis to identify the robust set of parameters

## Slide 11: Buildup/Washoff: Calibration Plots for TP
Reference: Technical Memos.pdf

## Slide 12: Opti-Tool: HRU Timeseries Development
Data Used
  Selected robust set of pollutant buildup & washoff parameters in calibrated SWMM model
  Regional representative landuse-based annual average pollutant load export rates (kg/ha/yr)
  Hourly precipitation and PET timeseries (1992 to 2014)
Summary Results
  Adjusted buildup parameters to match the simulated long-term annual average pollutant loading rate (kg/ha/yr)
  Compared the simulated EMC distribution against the observed EMC distribution for impervious land use types
  Developed HRU hourly timeseries for flow, TP, TN, and TSS

## Slide 13
Reference: Technical Memos.pdf

## Slide 14: Opti-Tool: HRU Types
Commercial/Industrial
High-Density Residential
Medium-Density Residential
Low Density Residential
Highway
Open Land
Forest
Agriculture
Forest Pervious
Agriculture Pervious
Developed Land Pervious – Hydrologic Soil Group A
Developed Land Pervious – Hydrologic Soil Group B
Developed Land Pervious – Hydrologic Soil Group C
Developed Land Pervious – Hydrologic Soil Group C/D
Developed Land Pervious – Hydrologic Soil Group D

## Slide 15: Opti-Tool: BMP Calibration
Data Used
  BMP design specifications (from the UNHSC)
  BMP monitoring data: flow and water quality (from the UNHSC)
BMP Parameterization
  Developed SUSTAIN models
  Calibrated water quality parameters (1st order decay and underdrain removal rate)
  Compared simulated BMP hydrograph and water quality performance against the observed BMP hydrograph and observed BMP efficiency
  Calibrated structural stormwater BMPs for flow, TP, TN, and TSS

## Slide 16: Bioretention: Hydrology Calibration

## Slide 17: Opti-Tool: BMP Performance Curve
Data Used
  Calibrated SUSTAIN model
  Calibrated hourly HRUs timeseries (1992 to 2014)
BMP Simulation
  Run BMP scenarios for a range of storage capacity and estimated the pollutant load reductions
  Developed BMP performance curve (pollutant load reduction vs storage capacity)
  Developed long-term cumulative pollutant load and runoff volume reduction performances for several categories of structural stormwater controls

## Slide 19: Opti-Tool: BMP Types
Bio-filtration
Enhanced Bio-filtration with Internal Storage Reservoir
Dry Pond
Grass Swale
Gravel Wetland
Infiltration Basin
Infiltration Chambers
Infiltration Trench
Porous Pavement
Sand Filter
Wet Pond

## Slide 20: Opti-Tool: BMP Cost Function
Combination of the Charles River Watershed Association and UNHSC costs estimates
Modified capital cost assessment (includes a fixed percentage for Design and Contingency Costs)
Maintenance hours (from the UNHSC)
Reference: Technical Memos.pdf
BMP Type | Cost ($/ft3) – 2016
Bioretention | $ 15.46
Dry Pond | $ 6.8
Enhanced Bioretention | $ 15.61
Infiltration Basin | $ 6.24
Infiltration Chamber | $ 67.85
Infiltration Trench | $ 12.49
Porous Pavement (Porous Asphalt Pavement) | $ 5.32
Porous Pavement (Pervious Concrete) | $ 18.07
Sand Filter | $ 17.94
Subsurface Gravel Wetland | $ 8.78
Wet Pond | $ 6.8

## Slide 21: Opti-Tool: Interfaces

## Slide 22: Planning Level: Two Approaches
BMP Storage Capacity
  Evaluate the BMP performance for a design criterion (e.g., capture 1 inch storm size)
  Evaluate the changes in water quality benefits as the BMP sizes are changed
  Identify the most cost-effective BMP storage capacity that meets the target pollutant load reduction
BMP Drainage Area
  Determine how much impervious drainage area would require treatment if specified BMP design capacities were selected
  Identify the extent of impervious area to be treated that can provide the target pollutant load reduction
  In this approach, both the BMP storage capacity and BMP cost are fixed

## Slide 23: Opti-Tool: Planning Level

## Slide 24: Opti-Tool: Planning Level – cont.

## Slide 25: Opti-Tool: Interfaces

## Slide 26: Opti-Tool: Implementation Level

## Slide 27: Opti-Tool: Implementation Level – cont.

## Slide 28: Opti-Tool: View Results
Cost $84.53 million to meet 52.1% average annual TP load reduction target
Cost saving of $47.5 million (56%) by lowering 10% of the numeric target (42.1%)

## Slide 29: Benefits of Opti-Tool
Accessible to all users with Microsoft Excel 2013 software
Represents actual regional precipitation conditions
Incorporates best available information on regional stormwater urban runoff nutrient quality for estimating the long-term surface runoff and pollutant loadings from different land uses
Incorporates best available information for estimating long-term cumulative nutrient load and runoff volume reduction performances for structural stormwater controls
Uses information which is being shared with other regional tool developers to promote the use of consistent and high quality data

## Slide 30: Benefits of Opti-Tool – cont.
Incorporates representative stormwater control units cost information with scaling function to account for specific conditions and development density
Includes flexibility to conduct either watershed planning level or detailed site specific design-level analyses
Performs optimization analyses to determine most cost-effective selection of structural stormwater controls for achieving pollutant loading and runoff flow related reduction targets
Results are consistent with loading rates and BMP performance documented in the EPA Region 1 MS4 permits

## Slide 31: Flexible to Adopt for Other Regions
Develop local weather data
  Hourly precipitation (in./hr)
  Daily temperature (min and max)
Run SWMM model (provided in the installation package)
  Local weather data (input)
  SWMM hourly HRU timeseries (output)
Run HRU utility tool (provided in the installation package)
  SWMM hourly HRU timeseries (input)
  Opti-Tool hourly HRU timeseries (output)
Update default data (provided in the installation package)
  HRU timeseries and local BMP cost function (optional)

## Slide 32: Feedback and Other Presentations
Questions or comments?
  Mark Voorhees (voorhees.mark@epa.gov)
Links to other presentations
  https://www.epa.gov/npdes/npdes-stormwater-webcasts